## Slide 1
TEAM DETAILS
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
4
Member 3
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
TECHTONICS
AKSHAYA SRELEKA P S
III YEAR
ASHWINKUMAR K
III YEAR
DHAMARAI KANNAN A
III YEAR
DHARSHAN S
III YEAR
CHENNAI INSTITUTE OF TECHNOLOGY
+91 7010449210
akshayasreleka2006@gmail.com

## Slide 2
PROBLEM STATEMENT
Drift-Sense: AI-Powered Navigation-Error Recovery for Wafer Inspection Tools
PROBLEM DESCRIPTION:
Given a high-magnification Reference Image and a 10× shrunk Search Image, the system must:
  Locate where the reference pattern appears inside the search image.
  Return the matching center coordinates (x, y) in pixels.
  Resolve multiple similar matches by selecting the candidate closest to the search-image center.
SOLUTION SUMMARY:
A physics-aware 5-phase cascade that recovers the correct SEM navigation site across magnification changes using multi-scale NCC, geometric verification, selective ML reranking, and sub-pixel Fourier refinement.
KEY RESULT:
98.33% Operational Accuracy (<5 px) | 86.67% High-Precision Accuracy (<1 px) | 0.7012 px Median Localization Error | 672.39 ms Mean Execution Latency

## Slide 3
PROPOSED END-TO-END WORKFLOW
INPUT CHALLENGES:
10× scale gap • SEM noise • scale/rotation variation • stage drift • periodic ambiguity
WHY CASCADE?
Fast NCC first → deeper processing only when ambiguity remains
DECISION LOGIC:
High confidence → Direct path
Low confidence / periodic ambiguity → Geometry → ML
OUTPUT:
Predicted (x, y) → Fine local refinement → Sub-pixel coordinate

## Slide 4
FINFET SYNTHETIC DATA DESIGN
CLASS | CLASS NAME | JUSTIFICATION
P1 | FIN_ARRAY | Multi-scale and angular alignment under directional gradient structure
P2 | FIN_CUT | Edge termination sensitivity and sub-pixel gap estimation
P3 | FIN_GATE | 2D spatial coherence and cross-junction tracking
P4 | CONTACT_ARRAY | Periodic lattice ambiguity and pitch-hop disambiguation
P5 | LOCAL_INTERCONNECT | Structural shape matching and local asymmetry
P6 | METAL_ROUTING | Multi-layer contrast and routing-pattern matching
P7 | ACTIVE_CELL | Asymmetric boundary localization
P8 | FINFET_FULL_CELL | Complex periodicity and multi-layer cell ambiguity

## Slide 5
SEM DEGRADATION & AUGMENTATION MODEL
DEGRADATION MODEL | RANGE / PURPOSE IN EVALUATION | WHAT IT TESTS
Poisson Shot Noise | 500–3500 e⁻/pixel | Robustness to electron-counting noise and low beam dose
Detector Noise | σ = 0.8–3.2 | Readout/detector noise
Beam Blur / PSF | σ = 1.0–2.5 px | Localization under reduced spatial sharpness
Scale Variation | 0.091–0.111 | Cross-magnification scale mismatch
Rotation | ±2.0° | Angular misalignment
Stage Drift | ±11 px | Spatial positioning error
Surface Charging | Scanline intensity modulation | Charging-induced appearance variation
[1] Goldstein et al. (2018)
Scanning Electron Microscopy and X-Ray Microanalysis
https://link.springer.com/book/10.1007/978-1-4939-6676-9
[2] Everhart & Thornley (1960)
Wide-band detector for micro-microampere low-energy electron currents
https://doi.org/10.1088/0950-7671/37/7/307
[3] Li, Zhang & Ding (2013)
Monte Carlo Simulation of CD-SEM Images for Linewidth and Critical Dimension Metrology
https://doi.org/10.1002/sca.21042
[4] Cazaux (1999)
Some considerations on the secondary electron emission, δ, from e− irradiated insulators
https://doi.org/10.1063/1.369239
CITATIONS

## Slide 6
LOCALISATION METHOD & DECISION RULE
PHASE | PURPOSE SUMMARY
P1 — Global Multi-Scale NCC | Generate potential match locations using multi-scale, multi-angle NCC and return Top-K candidates.
P2 — Geometry-Based Disambiguation | Verify structural and periodic consistency using spacing, alignment, local contrast and periodic candidate verification to eliminate false matches.
P5 — Siamese Metric Re-Ranking | Use Siamese CNN similarity to re-rank difficult candidates and select the most likely match.
P3 — Adaptive Fine Local Search | Refine the selected candidate using a local search window, fine-scale sweep and small angular variations.
P4 — Sub-Pixel Fourier Refinement | Refine the final peak using frequency-domain phase correlation and 2D interpolation for accurate sub-pixel coordinates.
Output | Return the final predicted coordinates (xₚᵣₑ𝒹, yₚᵣₑ𝒹).
Decision Rule:
If S_gate ≥ 0.65 AND Peak Gap ≥ 0.075 → accept the Top-1 NCC candidate and proceed directly to Phase 3 for fine localization.
Design Principle:
CLASSICAL FIRST → GEOMETRY WHEN AMBIGUOUS → ML AS SELECTIVE TIE-BREAKER → SUB-PIXEL REFINEMENT

## Slide 7
IMPLEMENTATION & EXECUTION COMMANDS
1. ENVIRONMENT & DEPENDENCIES
  Python-based implementation
  OpenCV / NumPy for image processing
  PyTorch for Siamese metric learning
  SciPy for numerical and Fourier refinement
  Matplotlib / visualization utilities for diagnostics
TRAINING & CALIBRATION — OFFLINE
Physics-Based Dataset
↓
Siamese Training
↓
Hard-Negative Mining
↓
Similarity Threshold Calibration
↓
Frozen Localization Model
Training is performed offline; the trained model is selectively invoked during inference.
COMMAND | FUNCTION
python generate_dataset.py | Generate synthetic SEM benchmark pairs
python localize.py | Run the 5-phase localization engine
python evaluate_predictions.py | Calculate accuracy and localization-error metrics
python app.py | Launch interactive diagnostic/dashboard interface
GENERATED OUTPUTS
  Predicted (x, y) coordinates
  Localization error
  Threshold-wise accuracy
  Runtime statistics
  Per-pattern performance
  Failure-case diagnostics
  Visualization / heatmaps
  Reproducibility

## Slide 8
EXPERIMENT SETUP & TEST DIVERSITY
EVALUATION DIMENSION | TEST DIVERSITY
Pattern Structure | FIN_ARRAY, FIN_CUT, FIN_GATE, CONTACT_ARRAY, LOCAL_INTERCONNECT, METAL_ROUTING, ACTIVE_CELL, FINFET_FULL_CELL
Magnification | 100× Reference → 10× Search field relationship
Spatial Variation | Continuous target locations with exact ground-truth (x, y)
Image Degradation | Noise, blur, scale variation, rotation, drift and charging
Periodic Ambiguity | Visually similar regions and hard-negative candidates
Boundary Cases | Targets near structural/boundary regions
Ground Truth | Exact target center recorded in Search-image coordinates
TEST DIVERSITY
8 Pattern Classes
+
Cross-Magnification
+
Controlled SEM Degradation
+
Spatial / Geometric Variation
+
Periodic Hard Negatives
↓
HELD-OUT LOCALIZATION BENCHMARK
EVALUATION PROTOCOL
120 unseen pairs • 8 patterns • 15/pattern • Exact GT coordinates
STRESS COVERAGE
Noise • Blur • Scale • Rotation • Drift • Charging • Boundary cases
KEY TEST
Can the system select the correct target when several visually similar candidates exist?

## Slide 9
THRESHOLD WISE ACCURACY, ERROR STATISTICS & RUNTIME
KEY PERFORMANCE HIGHLIGHTS
98.33%
Operational Accuracy < 5 px
86.67%
High Precision < 1 px
0.7012 px
Median Localization Error
672.39 ms
Mean Inference Latency
Overall Pass Rate
99.17% — 119 / 120 benchmark cases
METRIC | MEASURED VALUE | INDUSTRIAL STANDARD
Operational Accuracy (<5 px) | 98.33% (118/120) | ≥ 95.0%
Fine Review Accuracy (<2 px) | 98.33% (118/120) | ≥ 90.0%
High Precision Accuracy (<1 px) | 86.67% (104/120) | ≥ 75.0%
Sub-Pixel Accuracy (<0.5 px) | 30.83% (37/120) | ≥ 25.0%
Median Localization Error | 0.7012 px | < 1.0 px
Mean Localization Error | 1.5290 px | < 2.0 px
P95 Localization Error | 1.1829 px | < 3.0 px
Mean Execution Latency | 672.39 ms/pair | < 1000 ms

## Slide 10
ROBUSTNESS COMPARISON AND BASELINE ABLATION
APPROACH | STRENGTH | LIMITATION
Global Multi-Scale NCC | Fast candidate generation | Can produce multiple peaks in periodic layouts
Geometry-Based Disambiguation | Uses structural consistency | Activated only for ambiguous candidates
Siamese Metric Re-Ranking | Distinguishes visually similar candidates | More computationally expensive; used selectively
Fine Local Search | Improves local coordinate accuracy | Applied after candidate selection
Fourier Refinement | Provides sub-pixel peak refinement | Final localization refinement
INFERENCE PATH | SAMPLES | PERCENTAGE
NCC Direct | 114 / 120 | 95.00%
Geometry Verified | 1 / 120 | 0.80%
Siamese ML Re-ranked | 5 / 120 | 4.20%
NOISE TIER | DOSE | DETECTOR Σ | ACCURACY<1.0 PX
LOW | 3500 e⁻/px | 0.8 | 87.5%
MEDIUM | 2000 e⁻/px | 1.6 | 83.3%
HIGH | 1000 e⁻/px | 2.4 | 78.1%
SEVERE | 500 e⁻/px | 3.2 | 75.0%
LOCALIZATION METHOD COMPARISON
INFERENCE PATH UTILIZATION
ROBUSTNESS UNDER CONTROLLED NOISE
ROBUSTNESS COMPARISON & CASCADE PERFORMANCE
1. Localization Method Comparison
Classical NCC → Geometry → Siamese ML → Fine Search → Fourier Refinement
2. Inference Path Utilization
95.0% NCC Direct | 0.8% Geometry Verified | 4.2% Siamese ML
3. Robustness Under Controlled Noise
100% <5 px pass rate across all four noise tiers

## Slide 11
FAILURE CASE, LIMITATION & LEARNING
Periodic FinFET structure
↓
Target located near boundary
↓
Reduced / truncated contextual information
↓
Neighbouring periodic cell produces a stronger match
↓
Periodic ghost candidate selected
↓
66.03 px pitch jump
The failure corresponds approximately to one vertical periodic cell pitch, making this a structured ambiguity rather than random localization error
FAILURE MECHANISM
ATTRIBUTE | VALUE
Case | PAIR_110 — P8: FINFET_FULL_CELL
Ground Truth | (269.29, 305.97)
Prediction | (270.00, 372.00)
Localization Error | 66.03 px
WORST-CASE FAILURE: PERIODIC PITCH JUMP
Highly periodic layouts combined with insufficient boundary context can make an incorrect neighbouring cell appear more similar than the true target.
PRIMARY LIMITATION
High NCC confidence alone is not sufficient when multiple periodic candidates are structurally similar.
KEY LEARNING
  Larger macro-context around the target
  Asymmetric layout fiducials
  Peripheral boundary masking
  Improved periodic-cell disambiguation
NEXT IMPROVEMENTS
The observed error is a structured periodic pitch jump, indicating candidate-selection ambiguity rather than a general failure of the localization pipeline.
FAILURE CHARACTERIZATION

## Slide 12
CONCLUSION
METRIC | RESULT
Operational Accuracy <5 px | 98.33% (118/120)
Fine Review Accuracy <2 px | 98.33% (118/120)
High Precision <1 px | 86.67% (104/120)
Sub-Pixel <0.5 px | 30.83% (37/120)
Median Localization Error | 0.7012 px
Mean Localization Error | 1.5290 px
Mean Latency | 672.39 ms/pair
METRIC | RESULT
Operational Accuracy <5 px | 90.00% (36/40)
Standard Tolerance <4 px | 90.00% (36/40)
Fine Alignment <2 px | 90.00% (36/40)
High Precision <1 px | 72.50% (29/40)
Sub-Pixel <0.5 px | 25.00% (10/40)
Median Localization Error | 0.8233 px
  40 augmented RGB image pairs
  Same coordinate-localization objective
  Controlled visual variations introduced through augmentation
  Evaluation at <5 px, <4 px, <2 px, <1 px and <0.5 px thresholds
  Median localization error used as the central accuracy measure
FINAL BENCHMARK RESULTS — SEM
RGB OPTICAL BENCHMARK — EVALUATION SETUP
GITHUB LINK: https://github.com/DK-A/Techtonics_Drift-Sense_Wafer_Inspection_PS2
DEMO VIDEO LINK: https://drive.google.com/file/d/1sxvBWdj1c7RfX7oeG66R8FJaaMt8o1iI/view?usp=sharing